## Slide 1: Robotics Project Study of local path planning in a dining hall service robot scenario
Team 1
Jee Yong Park
Seungyoon Lee
Junhyeok Lim

## Slide 2: Summary
Aim: study & implement online dynamic path planning algorithms
Scenario: mobile robot for dining hall service (food delivery)
  Simulated environment and configuration – reasonably rescaled

## Slide 3: Scenario
Dining hall walkway, approx. 2m x 4m+, tables on either long edges
Customer orders via GUI
When ready to serve, waiter inputs table number via GUI and puts food on robot
Robot detects payload and knows when to start navigation
Robot navigates to designated table, avoiding unmapped static obstacles (chairs, bags, etc.) and dynamic obstacles (humans)
Robot detects if payload is off and knows when to return home
Similar procedure for returning trays
Experiment in scaled, simulated environment as a demonstration of the concept

## Slide 4
복도
테이블 1
테이블 3
카운터(wall)
Home
Wall
테이블 2

## Slide 5
테이블1
테이블2
테이블3
카운터
터틀봇
정면 조감도

## Slide 6
테이블1
테이블2
테이블3
카운터
터틀봇
wall
측면 조감도

## Slide 7: Configuration
Turtlebot3 Waffle Pi
Custom (printed or laser-cut) spring-suspended platform for payload placement & weight detection
2D LiDAR, IMU, RGB camera, load cell weight sensor
ROS Kinetic
  Mostly dependent on Turtlebot3 packages

## Slide 8: Framework

## Slide 9: Tasks proposed
Human interaction
  Automatic payload detection
  GUI for customer & waiter
Localisation & pose estimation
  Default method by 2D LiDAR + odometry fusion
Obstacle detection
  Default method for local costmap as baseline
Dynamic local path planning
  Main challenge: implement our own dynamic, online local path planner, compare behaviours

## Slide 10: Challenges
Custom local path planner
  Original plans: fuzzy logic & artificial potential field
  Scrapped due to difficulties with C++, ROS plugin, velocity control, etc.
Experimentation with other local planners
  TEB (time elastic band): harsh oscillation near obstacles
    Inaccurate model parameters of the robot
    Inadequate local costmap generation
    Heavy computation for ~8-year-old laptop
  MPC (model predictive control): unable to install package
Struggles with 3D printer

## Slide 11: Observations and evaluation
Satisfactory performance only achieved with DWA (baseline) local planner
Robot deals with dynamic obstacles at reasonable speed & distance with relative ease
Suboptimality, jitter and jerk found when running into unexpected obstacles
LiDAR + IMU fusion AMCL works with negligible error (max 10 cm)
Excessive load (1kg+) causes wheels to slip
2D LiDAR limits the use beyond idealised environment
Robot sometimes seems to “get lost” in finding target orientation

## Slide 12: Lessons and takeaways
Understanding of ROS
  Navigation stack and move_base
  Topics and action clients
  ROS file system
  Package creation and registration
  ROS plugins
  Use of rosbridge for interface with web-based applications
Simple solutions are often very effective compared to sophisticated, complex solutions